## Slide 1: Media Compression Techniques
Duc Nguyen
Tohoku Institute of Technology
Sendai, Japan

## Slide 2: Compression
The process of reducing the size of a data file
Types
  Lossless compression: Preserve all information of the source data
  Mainly for text, data files
  Ex: zip, gzip
  Lossy compression: Some information are lossed
  Mainly for image, audio, video
  Ex: mp3, mp4, aac

## Slide 3: Lossless Compression
Compress data by exploiting statistical redundancy in the source data
Run-length coding (Huffman code)
  Runs of data are stored as a single data value and count
Source data: AAABBCCCCDEFFF
Compressed data: 3A2B4C1D1E3F

## Slide 4: Lossy Compression
Dropping nonessential detail to reduce data size
  human eye is more sensitive to subtle variations in luminance than it is to the variations in color
Based on transform coding
  Fourier Series

## Slide 5: Image Compression: Basics
Human vision is insensitive to high spatial frequencies
JPEG Takes advantage of this by compressing high frequencies more coarsely and storing image as frequency data
JPEG is a “lossy” compression scheme.
Losslessly compressed image, ~150KB
JPEG compressed, ~14KB

## Slide 6: Digital Image Representation
JPEG can handle arbitrary color spaces (RGB, CMYK, YCbCr (separates colors into grayscale components)
Luminance/Chrominance commonly used, with Chrominance subsampled due to human vision insensitivity
Uncompressed spatial color data components are stored in quantized values (8, 16, 24bit, etc).

## Slide 7: Flow Chart of JPEG Compression Process
Divide image into 8x8 pixel blocks
Apply 2D Fourier Discrete Cosine Transform (FDCT) Transform
Apply coarse quantization to high spatial frequency components
Compress resulting data losslessly and store
8x8 pixel
blocks
FDCT
Frequency Dependent quantization
Zig-zag scan
Huffman encoding
JPEG syntax generator
Quantization Table
output

## Slide 8: Example of Frequency Quantization with 8x8 blocks
128 | 128 | 128 | 128 | 128 | 128 | 128 | 128
118 | 111 | 112 | 117 | 120 | 123 | 123 | 122
125 | 121 | 115 | 111 | 119 | 119 | 118 | 117
120 | 121 | 113 | 113 | 125 | 124 | 115 | 108
120 | 120 | 116 | 119 | 124 | 120 | 115 | 110
117 | 113 | 111 | 122 | 120 | 110 | 116 | 119
109 | 113 | 111 | 122 | 120 | 110 | 116 | 119
111 | 121 | 124 | 118 | 115 | 121 | 117 | 113
-80 | 4 | -6 | 6 | 2 | -2 | -2 | 0
24 | -8 | 8 | 12 | 0 | 0 | 0 | 2
10 | -4 | 0 | -12 | -4 | 4 | 4 | -2
8 | 0 | -2 | -6 | 10 | 4 | -2 | 0
18 | 4 | -4 | 6 | -8 | -4 | 0 | 0
-2 | 8 | 6 | -4 | 0 | -2 | 0 | 0
12 | 0 | 6 | 0 | 0 | 0 | -2 | -2
0 | 8 | 0 | -4 | -2 | 0 | 0 | 0
16 | 11 | 10 | 16 | 24 | 40 | 51 | 61
12 | 12 | 14 | 19 | 26 | 58 | 60 | 55
14 | 13 | 16 | 24 | 40 | 57 | 69 | 56
14 | 17 | 22 | 29 | 51 | 87 | 80 | 62
18 | 22 | 37 | 56 | 68 | 109 | 103 | 77
24 | 35 | 55 | 64 | 81 | 104 | 113 | 92
49 | 64 | 78 | 87 | 103 | 121 | 120 | 101
72 | 92 | 95 | 98 | 112 | 100 | 103 | 99
-5 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | -1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | -1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Quantization Matrix to divide by
Color space values (spatial data)
Quantized spatial frequency values
Color space values (spatial data)

## Slide 9: Scanning and Huffman Encoding
-5 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | -1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | -1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Spatial Frequencies scanned in zig-zag pattern (note high frequencies mostly zero)
Huffman encoding used to losslessly record values in table
0,2,1,-1,0,0,1,0,1,1,0,0,1,0,0,0,-1,0,0,… 0
Can be stored as:
(1,2),(0,1),(0,-1),(2,1),(1,1),(0,1),(0,1),(2,1),(3,1),EOB

## Slide 10: Examples of varying JPEG compression ratios
500KB image, minimum compression
40KB image, half compression
11KB image, max compression

## Slide 11: Close-up details of different JPEG compression ratios
Uncompressed image (roughness between pixels still visible)
Half compression, blurring & halos around sharp edges
Max compression, 8-pixel blocks apparent, large distortion in high-frequency areas

## Slide 12: Video Compression
Using strictly spatial redundancy (JPEG) gives video compression ratios from 7:1 to 27:1
Taking advantage of temporal redundancy in video gives 20:1 to 300:1 compression for H.261, or 30:1 to 100:1 for high quality MPEG-2

## Slide 13: Temporal Redundancy
Two consecutive images in a video have a lot of similarities
  Better to compress the “difference” images to reduce redundancy

## Slide 14: Exercise: Compressing video using FFMPEG
Install FFMPEG
Download sample video and ffmpeg using HTTPClient.java program
  sample video: input.mp4
  ffmpeg: ffmpeg.zip
Extract ffmpeg.zip, then copy input.mp4 into bin/ folder

## Slide 15
Open Command Prompt, go to ffmpeg/bin/ folder
Create raw video:
ffmpeg -i input.mp4 input.yuv

## Slide 16: Exercise: Compressing video using FFMPEG

## Slide 17: Exercise: Compressing video using FFMPEG
Calculate average video bitrate (Mbit/s)
bitrate (h264) = ?
bitrate (h265) = ?

## Slide 18: Exercise: Compressing video using FFMPEG
Adjust compressed video quality
  In ffmpeg, output video quality is controlled by Constant Rate Factor (CRF) parameter, which takes value from 1-51. Default value: 23
  ffmpeg -i input.mp4 -c:v h264 -crf 23 crf23.mp4

## Slide 19: Exercise: Compressing video using FFMPEG
Change the value of the crf parameter and compare 1) compressed video size, 2) compressed video PSNR, and compression ratio
CRF | Compressed video size | Compressed video PSNR | Compression ratio
0 |  |  | 
18 |  |  | 
23 |  |  | 
28 |  |  | 
51 |  |  |